## Slide 1: Investigating Feasibility of QUIC on Constrained Devices
Student: Mikhail Dyuldin
Supervisor: Stefan Weber
    Date 20/07/2021

## Slide 2: Overview
Background
Challenges
Experiments
Results
Evaluation

## Slide 3: Background
Microcontroller – 2 ESP32 DevKitC’s
2 Cores 80-240MHz Adjustable (160Mhz used)
4MB Flash
8MB PSRAM
Micro USB powered
Comes installed with an ESP32-WROVER-E Module
Allowing communication over Wi-Fi and Bluetooth.
This chip was chosen based on it having this capability.
ESP32-WROVER-E

## Slide 4: Background
Frameworks
The ESP32 for this project runs on their native ESP-”IDF”
Many people have heard of Arduino and it is a great framework for beginners but doesn’t allow the fidelity required to fine-tune the tasks running on the MCU.
Benefits: adjusting build type, partition tables for storage, Http client and server behaviour and many more
VS

## Slide 5: Background
Protocols
HTTP/0.9
HTTP/1.0
HTTP/1.1
HTTP/2
HTTP/3

## Slide 6: Background
Protocols
HTTP/0.9
GET /my-page.html

## Slide 7: Background
Protocols
Persistent Connections
3-Way Handshakes
Slow start
informit.com

## Slide 8: Background
Protocols
Wireshark chunked packet inspection
Data sent out faster with Chunked Transfer-Encoding
No need to buffer data before sending it

## Slide 9: Background
Protocols
informit.com
Pipelining
Below is an experiment where the ESP
requests files in batches of 55. One does not
Have pipelining and the other does.
(No Pipelining)
(Pipelining)

## Slide 10: Background
Protocols
SSL Handshake
msdn.microsoft.com

## Slide 11: Background
Protocols
HTTP/2
blog.cloudflare.com

## Slide 12: Background
Protocols
HTTP/2
Single Connection
Prioritization
Binary
Header Compression
Server Push

## Slide 13: Background
QUIC
Multiplexing with multi-streaming
Single connection
Ably.com

## Slide 14: Background
QUIC
Cryptography
Improved Server PUSH
Better Header Compression
Ably.com

## Slide 15: Background
Microcontroller Tie-in
CPU
RAM
PACKET
PACKET
PACKET
PACKET
PACKET
Integrify.com
CPU 160MHz
520KB (total) SRAM
320KB (usable) SRAM

## Slide 16: Background
Microcontroller Tie-in
Bytes 1 through 512 have been transmitted (and pushed to the application using the TCP PSH flag) and have been acknowledged by the destination host.
The window is 2,048 bytes long.
Bytes 513 through 1,536 have been transmitted but have not been acknowledged.
Bytes 1,537 through 2,560 can be transmitted immediately.
Once an acknowledgement is received for bytes 513 through 1,536, the window will move 1,024 bytes to the right, and bytes 2,561 through 3,584 may then be sent.
Embedded.com
Text + Image

## Slide 17: Background
Microcontroller Tie-in
Window: 5744
Window: 64723
Window: 5490
Window: 64646
Window: 3188
Window: 64492
Window: 64492
Window: 632

## Slide 18: Challenges
Quant was implemented over Real Time Operating System (RIOT OS) on an ESP32 by Lars.
RIOT-OS based on boards with no Wi-Fi, needed raspberry pi intermediary connect via Bluetooth to MCU and forward over Wi-Fi to server
Quant had picotls and picoquic dependencies which would take a large amount of time to port
QUIC Implementation by Lars Eggert: Quant

## Slide 19: Experiments
Clients
Servers
HTTP_request
HTTPS_request
HTTPS_mbedtls
UDP_client
HTTP_file_server
HTTPS_server
UDP_server

## Slide 20: Experiments
Clients
Servers
HTTP_request
HTTPS_mbedtls
UDP_client
HTTP_file_server
HTTPS_file_server
UDP_server

## Slide 21: Experiments
Clients
Servers
HTTP_request
HTTPS_mbedtls
UDP_client
CURL
Netcat
HTTP_file_server
HTTPS_file_server
UDP_server
Nginx
Netcat

## Slide 22: Experiments
Clients
Severs

## Slide 23: Experiments
IPv4 = 255.255.255.0 => IPv4 = 255.255.255.255

## Slide 24: Experiments
Experiments to test :
Http1.0 & Http1.1
TLS
Every combination of connections with constrained and not constrained devices, total of 8 batch tests
Each batch test is broken down into 3 separate tests where 1KB, 10KB, and 100KB are sent consecutively 55 times
The measurements taken are based around the speed of the connections.
As for the header sizes, UDP had slightly smaller header sizes compared to TCP which meant that their MTU was slightly bigger, increasing throughput.

## Slide 25: Results /Evaluation
Chart: 100KB batch stress test
| ESP req ESP | ESP req PC | Curl req ESP | Curl req PC
HTTP | 703.6662 | 490.5429 | 20.5985 | 0.716
HTTPS | 795.666 | 563.91 | 60.67 | 0.742

## Slide 26: Results /Evaluation
Chart: FULL UDP BATCH TEST RESULTS
| ESP to ESP | Ncat to ESP | ESP to Ncat | Ncat to Ncat
1KB | 0.034489 | 13.3043 | 0.021806 | 0.008985
10KB | 0.096762 | 31.199 | 0.12716 | 0.018327
100KB | 0 | 175.4831 | 0 | 0.8394

## Slide 27: Results /Evaluation
Chart: ESP REQUESTS ESP
| HTTP | HTTPS
1KB | 7.2062 | 15.4476
10KB | 72.493 | 77.4867
100KB | 703.6662 | 795.6664

## Slide 28: Results /Evaluation
Chart: ESP REQUESTS PC
| HTTP | HTTPS
1KB | 6.5142 | 8.9635
10KB | 50.6216 | 59.1985
100KB | 490.5429 | 563.911

## Slide 29: Results /Evaluation
Chart: CURL REQUESTS ESP
| HTTP | HTTPS
1KB | 10.3436 | 13.0538
10KB | 6.4765 | 16.8685
100KB | 20.5985 | 60.6705

## Slide 30: Results /Evaluation
Chart: CURL REQUESTS PC
| HTTP | HTTPS
1KB | 0.049514 | 0.059916
10KB | 0.055533 | 0.066367
100KB | 0.71622 | 0.74287

## Slide 31: Results /Evaluation
Chart: Hotspot Latency Difference
| Hotspot | Direct
1KB | 7.888 | 6.048

## Slide 32: Conclusion
Great Improvements in Performance for HTTP/2 and HTTP/3
Not completely mitigating the constrained nature of MCU’s
Future Work:
New and improved UDP implementation with PSRAM and higher CPU clock speed

## Slide 33
Thank You!
Questions?